## Slide 1: The Basic of VHDL
디지털 전자회로 설계
박 창대

## Slide 2
1. Introduce basic VHDL constructs
2. Introduce the VHDL simulation cycle and timing model
3. Illustrate VHDL’s utility as digital hardware description language

## Slide 3: Module Outline
Introduction
VHDL Design Example
VHDL Model Components
  Entity Declarations
  Architecture descriptions
  Timing Model
Basic VHDL Constructs
  Data Types
  Objects
  Sequential and concurrent statements
  Package and libraries
  Attributes
  Predefined operators
Examples
Summary

## Slide 4: Introduction
VHDL Design Example
VHDL Model Components
Basic VHDL Constructs
Examples
Summary

## Slide 5
In a survey of 71 US universities
  44% have no training on or use of VHDL in any undergraduate EE course
  45% have no faculty members who can teach VHDL
  14% of the graduating seniors have a working knowledge of VHDL and only 8% know Verilog
However , 1994 survey, 85% of the engineers surveyed were designed and reported
  55% were familiar with EDIF
  55% were familiar VHDL
  33% were familiar with Verilog

## Slide 6
VHDL is an international IEEE standard specification language for describing digital hardware used by industry worldwide
  VHDL is an acronym for VHSIC( Very High Speed Integrated Circuit) Hardware Description Language
VHDL enables hardware modeling from the gate to system level
VHDL provides a mechanism for digital design and reusable design documentation

## Slide 7
Gate-Level Design in the 1980’s
High-Level Design in the 1990’s
Arch.
Design
Gate-Level
Implementation
Test
Implementation
Physical
Design
Comparing ASIC Design Cycles

## Slide 8
Reduce prototype turns
Less time in the Lab.
Design before silicon available
Verify design before board layout
Verify ASICs and programmable before fabrication
Development of software before PCB
Faster time-to-market ( concurrent Engineering)
Improved product quality
Fewer cuts and jumps on board
Discover error in Lab - not in the field
Better price/performance
Higher clock rates
ASIC Complexity increasing
Why is High-Level Simulation Required ?

## Slide 9
1990’s
(106 Gates)
1980’s
(105 Gates)
1970’s
(103 Gates)
HDL-Level Design
Gate-Level Design
Layout Design
Place & Layout
Synthesis
Synthesis Technology

## Slide 10
u-p
cache
I/O,Buf
DRAM
wait until CLK =1
STR_PTR<=N
end process;
N<=STR_PTR+1;
SI:0100010
SI:0100010
Layout
HDL Design
Entity
Simulation
System Design
Verification
Synthesis
RTL Optimization
HDL Translation
Logic Optimization
Test Generation
Simulation
Implemention
Verification
New Design Flow

## Slide 11: VHDL’s History
Very High speed Integrated Circuit(VHSIC) Program
  Launched in 1980
  Aggressive effort to advanced state of the art
  Object was to achieve significant gains in VLSI technology
  Need for common description language
  $17 Million for direct VHDL development
  $16 Million for VHDL design tools

## Slide 12: VHDL’s History(Cont.)
In 1983, a team of Intermetrics, IBM and TI were awarded a contract to develop VHDL
In 1985, the final version of the language under government contract was released: VHDL Version 7.2
In 1987, VHDL became IEEE standard 1076-1987 and in 1988 an ANSI standard
In 1993, VHDL was re-standardized to clarify and enhance the language

## Slide 13: Additional Benefits of VHDL
Allows for various design methodologies
Provides technology independence
describes a wide variety of digital hardware
Eases communication through standard language
Allows for better design management
Provides a flexible design language
Has given rise to derivative standards :
  WAVE, VITAL, analog VHDL

## Slide 14: Putting It All Together
Package
Entity
Architecture
Architecture
Architecture
Concurrent
Statements
Process
Sequential
Statements
Generic
Ports
Concurrent
Statements

## Slide 15
New Design Flow
u-p
cache
I/O,Buf
DRAM
wait until CLK =1
STR_PTR<=N
end process;
N<=STR_PTR+1;
SI:0100010
SI:0100010
Layout
HDL Design
Entity
Simulation
System Design
Verification
Synthesis
RTL Optimization
HDL Translation
Logic Optimization
Test Generation
Simulation
Implemention
Verification

## Slide 16
RTL VHDL
Source
RTL
Simulation
Function
OK?
Translation
to Gates
Gate-level
Optimization
Gate-level
Simulation
Speed &
Function
OK?
Gate-level
sign-Off
Synthesis
No
Yes
No
Yes
HDL Design Methodology

## Slide 17: VHDL Design Example
Problem : Design a single bit half adder with carry and enable
Specifications
  Inputs and outputs are each one bit
  When enable is high, result gets x plus y
  When enable is high, carry gets any carry of x plus y
  Outputs are zero when enable input is low
Half Adder
x
y
enable
carry
result

## Slide 18: VHDL Design Example: Entity Declaration
As a first step, the entity declaration describes the interface of the component
  input and output ports are declared
ENTITY half_adder IS
PORT( x, y, enable : IN BIT;
carry, result : OUT BIT);
END half_adder;
Half Adder
x
y
enable
carry
result

## Slide 19: VHDL Design Example: Behavioral Specification
A high level description can be used to describe the function of the adder
ARCHITECTURE half_adder_a OF half_adder IS
BEGIN
PROCESS ( x, y, enable)
BEGIN
IF enable = ‘1’ THEN
result <= x XOR y;
carry <= x AND y;
ELSE
carry <= ‘0’;
result <= ‘0’;
END IF;
END PROCESS;
END half_adder_a;

## Slide 20: VHDL Design Example: Data Flow Specification
ARCHITECTURE half_adder_b OF half_adder IS
BEGIN
carry <= enable AND (x AND y);
result <= enable AND (x XOR y);
END half_adder_b;
A Second method is to use logic equations to develop a data flow description
Again, the model can be simulated at this level to confirm the logic equations

## Slide 21: VHDL Design Example: Structural Specification
At a third method, a structural description can be created from pre-described components
These gates can be pulled from a library of parts
x
y
enable
result
carry

## Slide 22: VHDL Design Example: Structural Specification(Cont.)
ARCHITECTURE half_adder_c OF half_adder IS
Component and2
PORT(in0, in1 : IN BIT;
out0 : OUT BIT);
END COMPONENT;
Component and3
PORT(in0, in1, in2 : IN BIT;
out0 : OUT BIT);
END COMPONENT;
Component xor2
PORT(in0, in1 : IN BIT;
out0 : OUT BIT);
END COMPONENT;
-- next continued

## Slide 23
FOR ALL : and2 USE ENTITY gate_lib.and2_Nty(and2_a);
FOR ALL : and3 USE ENTITY gate_lib.and3_Nty(and3_a);
FOR ALL : xor2 USE ENTITY gate_lib.xor2_Nty(xor2_a);
SIGNAL xor_res : BIT;
BEGIN
A0 : and2 PORT MAP (enable, xor_res, result);
A1 : and3 PORT MAP (x,y, enable, carry);
X0 : and2 PORT MAP (x,y, xor_res);
END half_adder_c;

## Slide 24: VHDL Model Components
A complete VHDL component description requires a VHDL entity and a VHDL architecture
  The entity defines a component’s interface
  The architecture defines a component’s function
Several alternative architectures may be developed for use with the same
Three areas of description for a VHDL component
  structural descriptions
  Behavioral descriptions
  Timing and delay description

## Slide 25: VHDL Model Components (Cont.)
Fundamental unit for component behavior description is the process
  Process may be explicitly or implicitly defined and are packaged in the architecture
Primary communication mechanism is the signal
  Process executions result in new values being assigned to signals which are then accessible to other processes
  Similarly, a single may be accessed by a process in another architecture by connecting the signal to ports in the entities associated with the two architectures
  Example signal assignment statement :
Output <= My_id +10;

## Slide 26: Entity Declarations
The primary purpose of the entity is to declare the signals in the component’s interface
  The interface signals are listed in the PORT clause
    In this respect, the entity is akin to the schematic symbol for the component
  Additional entity clauses and statement will be introduced later in this and subsequent modules

## Slide 27: Entity Declarations Port Clause
PORT clause declares the interface signals of the object to the outside world
Three parts of the PORT clause
  Name
  Mode
  Data Type
Example PORT clause
  Note port signals(I.e. ‘port’) of the same mode and type or subtype may be declared on the same line
PORT ( input : IN BIT_VECTOR(3 DOWNTO 0);
ready, output : OUT BIT);
PORT (signal_name : mode data_type);

## Slide 28: Entity Declarations Port Clause (Cont.)
The port mode of the interface describes the direction in which data travels with respect to the component
The five available port modes are :
  In-data comes in this port and can only be read
  Out-data travels out this port
  Buffer-data may travel in either direction, but only one signal driver may be on at any one time
  In out-data may travel in either direction with any number of active drivers allowed ; requires a Bus Resolution Function
  Linkage-direction of data flow is unknown

## Slide 29
Port
Design block과의 연결
IN input
OUT output
INOUT bidirection
BUFFER output and read 가능
IN
OUT
INOUT
BUFFER

## Slide 30: Entity Declarations Generic Clause
Generics may be used for readability, maintenance and configuration
Generic clause syntax
if optional default_value missing in generic clause declaration, it must be present when component is to be used (I.e. instantiated)
Generic clause example :
The generic My_ID, with a default value of 37, can be referenced by any architecture of the entity with this generic clause
GENERIC (generic_name : type [ :=default_value]);
GENERIC (My_ID : INTEGER :=37);

## Slide 31
ARCHITECTURE BODY
회로의 실질적인 동작이나 연결 상태 등을 표현
하나의 entity에 복수개의 architecture 사용 가능
architecture 동작 표현 이름 is
[선언문]
begin
동작 표현
end entity이름

## Slide 32: Architecture Bodies
Describe the operation of the component
Consist of two parts :
  Declarative part -- includes necessary declarations, e.g. :
    type declarations, signal declarations, component declarations, subprogram declarations
  Statement part -- includes statements that describe organization and/or functional operation of component, e.g. :
    concurrent signal assignment statements, process statements, component instantiation statements
ARCHITECTURE half_adder_d OF half_adder IS
signal xor_res : BIT;
BEGIN
carry <= enable AND (x AND y);
result <= enable AND xor_res;
xor_res <= x XOR y;
END half_adder_d;

## Slide 33: Structural Descriptions
Pre-defined VHDL components are ‘instantiated’ and connected together
Structural descriptions may connect simple gates or complex, abstract components
Mechanisms for supporting hierarchical description
Mechanisms for describing highly repetitive structures easily

## Slide 34: Behavioral Descriptions
VHDL provides two styles of describing component behavior
  Data Flow : concurrent signal assignment statements
  Behavioral : processes use to describe complex behavior by means of high-level language constructs
    variables, loops, if-then-else statements, etc.
A behavioral model may bear little resemblance to system implementation
  structure not necessarily implied
Behavioral
Description
input
output

## Slide 35: Timing Model
VHDL uses a simulation cycle to model the stimulus and response nature of digital hardware
Start simulation
Update signal
Execute process
End simualtion
delay

## Slide 36: Delay Type
All VHDL signal assignment statements prescribe an amount of time that must transpire before the signal assumes its new value
This prescribed delay can be in one of three forms :
  Transport - prescribes propagation delay only
  Inertial - prescribes minimum input pulse width and propagation delay
  Delta - the default if no delay is explicitly specified
delay
input
output

## Slide 37: Transport Delay
-- TRANSPORT must be specified
Output <= TRANSPORT NOT Input AFTER 10 ns;
Delay must be explicitly specified by user
  Keyword “TRANSPORT” must be used
Signal will assume its new value after specified delay
delay
input
output
input
output

## Slide 38: Inertial Delay
Provides for specification of input pulse width, I.e. ‘inertial’ of output, and propagation delay :
Inertial delay is default and REJECT is optional :
Output <= TRANSPORT NOT Input AFTER 10 ns;
-- Propagation delay and minimum pulse width are 10 ns
delay
input
output
input
output
Target <= [REJECT time_expression] INERTIAL waveform;

## Slide 39: Inertial Delay (Cont.)
Example of gate with ‘inertia’ smaller than propagation delay
  e.g. Inverter with propagation delay of 10 ns which suppresses pulses shorter than 5 ns
Note that REJECT feature is new to VHDL 1076-1993
Output <= REJECT 5 ns INERTIAL NOT Input AFTER 10 ns;
input
output
0 5 10 15 20 25 30

## Slide 40: Delta Delay
Default signal assignment propagation delay if no delay is explicitly prescribed
  VHDL signals assignment cannot take place immediately
  Delta is an infinitesimal VHDL time unit so that all signal assignment can result in signals assuming their values at some future time
  E.g.
Support a model of concurrent VHDL process execution
  Order in which processes are executed by simulator does not affect simulation output
Output <= NOT Input;
--Output assumes new value in one delta cycle

## Slide 41: Delta Delay
What is the behavior of C ?
NAND gate evaluated first :
IN : 1->0
A : 0->1
B : 1->0
C : 0->0
AND gate evaluated first :
IN : 1->0
A : 0->1
C : 0->1
B : 1->0
C : 1->0
IN : 1->0
1
A
C
B

## Slide 42: Delta Delay An Example with Delta Delay
Using delta delay scheduling
Time Delta Event
0 ns 1 IN : 1-> 0
eval INVERTER
2 A : 0->1
eval NAND, AND
3 B : 1->0
C : 0->1
eval AND
4 C : 1->0
1 ns
IN : 1->0
1
A
C
B

## Slide 43: Data Types
All declarations VHDL ports, signals, and variables must specify corresponding type or subtype
Types
Acess
Composite
Record
Array
Scalar
Integer
Real
Enumerated
Physical

## Slide 44
Scalar Type
Enumeration Type : BIT, BOOLEAN, CHARACTER
Integer Type : INTEGER
Floating : REAL
Physical : UNIT : TIME, DISTANCE
Composition Type
Array Type
Constraint : TO, DOWNTO
Unconstraint : BIT_VECTOR, STRING
Record Type : RECORD
File Type : FILE
Data Types

## Slide 45: VHDL Data Types Scalar Types
Integer
  Minimum range for any implementation as defined by standard : -2,147,483,647 to 2,147,483,647
  Example assignments to a variable of type integer :
ARCHITECTURE test_int OF test_int IS
BEGIN
PROCESS (X)
VARIABLE a : INTEGER;
BEGIN
a := 1; --OK
a := -1; --OK
a := 1.0; --illegal
END PROCESS;
END test_int;

## Slide 46: VHDL Data Types Scalar Types (Cont.)
Real
  Minimum range for any implementation as defined by standard : -1.0E38 to 1.0E38
  Example assignments to a variable of type integer :
ARCHITECTURE test_int OF test IS
BEGIN
PROCESS (X)
VARIABLE a : REAL;
BEGIN
a := 1.3; --OK
a := -7.5; --OK
a := 1; --illegal
a := 1.7E13; --OK
a := 5.3 ns; --illegal
END PROCESS;
END test_int;

## Slide 47: VHDL Data Types Scalar Types (Cont.)
Enumerated
  use specifies list of possible values
  example declaration and usage of enumerated data type
TYPE binary IS ( ON, OFF);
……. Some statements ...
ARCHITECTURE test_enum OF test IS
BEGIN
PROCESS (X)
VARIABLE a : binary;
BEGIN
a := ON; --OK
………..
a := OFF; --OK
………..
END PROCESS;
END test_enum;

## Slide 48: VHDL Data Types Scalar Types (Cont.)
Physical
  require associated units
  range must be specified
  example of physical type declaration :
TYPE resistance IS RANGE 0 TO 10000000
UNITS
ohm; --ohm
Kohm = 1000 ohm;
Mhom = 1000 Kohm;
END UNITS;
Time is the only physical type predefined in VHDL standard:

## Slide 49: VHDL Data Types Composite Types
Array
  Used to group elements of the same type into a single VHDL object
  Range may be unconstrained in declaration
    Range would be then be constrained when array is used
  Example declaration for one-dimensional array (vector)
TYPE data_bus IS ARRAY( 0 TO 31) OF BIT;
0
… array values …
1
VARIABLE X : data_bus;
VARIABLE Y : BIT;
Y := X(12); --Y gets value of element at index 12
0
31

## Slide 50: VHDL Data Types Composite Types(Cont.)
Example one-dimensional array using DOWNTO :
TYPE reg_type IS ARRAY( 15 DOWNTO 0) OF BIT;
0
… array values …
1
VARIABLE X : reg_type;
VARIABLE Y : BIT;
Y := X(4); --Y gets value of element at index 4
14
0
DOWNTO keyword must be used if leftmost index is grater than rightmost index
  ‘Big-endian” bit ordering, for example

## Slide 51: VHDL Data Types Composite Types(Cont.)
Records
  Used to group elements of possibly different types into a single VHDL object
  Elements are indexed via field names
  Examples of record declarations and usage :
TYPE binary IS ( ON, OFF);
TYPE switch_info IS
RECORD : binary;
IDnumber :INTEGER;
END RECORD;
VARIABLE switch : swtich_info;
switch.status := ON; --status of the switch
switch.IDnumber := 30; --e.g. number of the switch

## Slide 52: VHDL Data Types Access Type
Access
  Analogous to pointers in other language
  Allows for dynamic allocation of storage
  Useful for implementing queues, fifos, etc

## Slide 53: VHDL Data Types Subtypes
Subtype
  Allows for user defined constrains on a data type
    e.g. a subtype based on an unconstrained VHDL type
  May include entire range off base type
  Assignments that are out of the subtype range are illegal
    Range violation detected at run time rather than compile time because only base type is checked at compile time
  Subtype declaration syntax :
SUBTYPE name IS base_type RANGE <user range>;
  Subtype example :
SUBTYPE first_ten IS INTEGER RANGE 0 TO 9;

## Slide 54: VHDL Data Types Summary
All declarations of VHDL ports, signals, and variables must included their associated type or subtype
Three forms of VHDL data types are :
  Access -- pointers for dynamic storage allocation
  Scalar -- included integer, Real, Enumerated, and Physical
A set of built-in data types are defined in VHDL standard
  user can also define own data types and subtypes

## Slide 55: VHDL Objects
There are four types of objects in VHDL
  Constants
  Variable
  Signals
  Files
The scope of an object is as follows :
  Objects declared in a package are available to all VHDL descriptions that use package
  Objects declared in an entity are available to all architecture associated with that entity
  Objects declared in an architecture are available to all statements in that architecture
  Objects declared in a process are available only within that process

## Slide 56: VHDL Objects Constants
Name assigned to a specific value of a type
Allow for easy update and readability
Declaration of constant may omit value so that the value assignment may be deferred
  Facilitates reconfiguration
Declaration syntax :
CONSTANT constant_name : type_name [ :=value];
Declaration examples :
CONSTANT PI : REAL := 3.14;
CONSTANT SPEED : INTEGER;

## Slide 57: VHDL Objects Variables
Provide convenient mechanism for local storage
  e.g. loop counters, intermediate values, etc.
Scope is process in which they are declared
  VHDL ‘93 provides for global variables, to be discussed in the advanced concepts in VHDL module
All variable assignments take place immediately
  No delta or user specified delay incurred
Declaration syntax :
VARIABLE variable_name : type_name [ :=value];
Declaration examples :
VARIABLE opcode : BIT_VECTOR(3 DOWNTO 0) := “0000”;
VARIABLE freq : INTEGER;

## Slide 58: VHDL Objects Signals
Used for communication between VHDL components
Real, Physical signals in system often mapped to VHDL signals
All VHDL signal assignments require either delta cycle or user-specified delay before new value is assumed
Declaration syntax :
SIGNAL signal_name : type_name [ :=value];
Declaration and assignment examples :
SIGNAL brdy : BIT;
brdy <= ‘0’ AFTER 5 ns, ‘1’ AFTER 10 ns;

## Slide 59: VHDL Objects Signals and Variables
This example highlights the difference between signals and variables
ARCHITECTURE test1 OF mux IS
SIGNAL x : BIT := ‘1’:
SIGNAL y : BIT := ‘0’:
BEGIN
PROCESS(in_sig, x, y)
BEGIN
x <= in_sig XOR y;
y <= in_sig XOR x;
END PROCESS;
END test1;
ARCHITECTURE test2 OF mux IS
SIGNAL y : BIT := ‘0’:
BEGIN
PROCESS(in_sig, y)
VARIABLE x : BIT := ‘1’;
BEGIN
x := in_sig XOR y;
y <= in_sig XOR x;
END PROCESS;
END test2;
Assuming a 1 to 0 transition on in_sig, what are the resulting values for y in the both cases ?

## Slide 60: VHDL Objects Signals vs Variables
A key difference between variables and signals is the assignment delay
ARCHITECTURE sig_ex OF test IS
SIGNAL a, b, c, out_1, out_2 : BIT :
BEGIN
PROCESS(a, b, c, out_1)
BEGIN
out_1 <= a AND b;
out_2 <= out_1 XOR c;
END PROCESS;
END sig_ex;
Time a b c out_1 out_2
0 0 1 1 1 0
1 1 1 1 1 0
1+d 1 1 1 0 0
1+2d 1 1 1 0 1

## Slide 61: VHDL Objects Files
Files provide a way for a VHDL design to communicate with host environment
File declarations make a file available for use to a design
Files can be opened for reading and writing
  In VHDL87, files are opened and closed when their associated objects come into and out of scope
  In VHDL93 explicit FILE_OPEN() and FILE_CLOSE() procedures were added
The package TEXTIO defines more powerful routines handling IO of text files

## Slide 62: Simulation Cycle Revisited Sequential vs Concurrent Statements
VHDL is inherently a concurrent language
  All VHDL processes execute concurrently
  Concurrent signal assignment statements are actually one-line processes
VHDL statements execute sequentially within a process
  Supports various levels of abstraction
  Supports modeling of concurrent and sequential events as observed in real systems

## Slide 63: Concurrent Statements
Basic granularity of concurrency is the process
  Processes are executed concurrently
  Concurrent signal assignment statements are one-line processes
Mechanism for achieving concurrency :
  Processes communicate with other via signals
  Signal assignments require delay before new value is assumed
  Simulation time advances when all active processes complete
  Effect is concurrent processing
    I.e. order in which processes are actually executed by simulator does not affect behavior
Concurrent VHDL statements include :
  Block, process, assert, signal assignment, procedure call, component instantiation

## Slide 64: Sequential Statements
Statements inside a PROCESS execute sequentially
ARCHITECTURE sequential OF test_mux IS
BEGIN
select_proc : process(x,y)
BEGIN
if (select_sig = ‘0’) THEN
z <= x;
ESLEIF (select_sig = ‘1’) THEN
z <= y;
ELSE
z <= “xxxx”;
END IF;
out_1 <= a AND b;
out_2 <= out_1 XOR c;
END PROCESS select_proc;
END sequential;

## Slide 65: Package and Libraries
User defined constructs declared inside architectures and entities are not visible to other VHDL components
  Scope of subprograms, user defined data types, constructs, and signals is limited to the VHDL components in which they are declared
Packages and libraries provide the ability to reuse constructs in multiple entities and architectures
  Items declared in packages can be used (I.e. included) in other VHDL components

## Slide 66: Packages
Packages consist of two parts
  Package declaration - contains declarations of objects defined in the package
  Package body - contains necessary definitions for objects in package declaration
    e.g. subprogram descriptions
Examples of VHDL items included in packages :
  Basic declarations  Single declarations
  Constants  Attribute declarations
  Subprogram  Component declarations
  Use clause

## Slide 67: Packages Declaration
An example of a package declaration :
PACKAGE my_stuff IS
TYPE binary IS (ON, OFF);
CONSTANT PI : REAL := 3.14;
CONSTANT My_ID : INTEGER;
PROCEDURE add_bits3 (SIGNAL a, b, en : IN BIT;
SIGNAL temp_result, temp_carry : OUT BIT);
END my_stuff;
Note some items only require declaration while others need further detail provide in subsequent package body
  for type and subtype definitions, declaration is sufficient
  subprograms require declarations and descriptions

## Slide 68: Packages package body
The package body includes the necessary functional descriptions for objects declared in the package declaration
  e.g. subprogram descriptions, assignments to constants
PACKAGE BODY my_stuff IS
CONSTANT My_ID : INTEGER := 2;
PROCEDURE add_bits3 (SIGNAL a, b, en : IN BIT;
SIGNAL temp_result, temp_carry : OUT BIT) IS
BEGIN
temp_result <= ( a XOR b) AND en;
temp_carry <= a AND b AND en;
END my_stuff;

## Slide 69: Packages Use clause
Packages must be made visible before their contents can be used
  The USE clause makes packages visible to entities, architectures, and other packages
-- use only the binary and add_bits3 declarations
USE my_stuff.binary, my_stuff.add_bits3;
….. ENTITY declaration ….
….. ARCHITECTURE declaration ….
-- use all of the declarations in package my_stuff
USE my_stuff.ALL;
….. ENTITY declaration ….
….. ARCHITECTURE declaration ….

## Slide 70: Libraries
Analogous to directories of files
  VHDL libraries contain analyzed (I.e. compiled ) VHDL entities, architectures, and packages
Facilitate administration of configuration and revision control
  e,g. libraries of previous designs
Libraries accessed via an assigned logical name
  Current design unit is compiled into the Work library
  Both Work and STD libraries are always available
  Many other libraries usually supplied by VHDL simulator vendor
    e.g. proprietary libraries and IEEE standard libraries

## Slide 71: Attributes
Attributes provide information about certain items in VHDL, e.g :
  Types, subtypes, procedures, functions, signals, variables, constants, entities, architectures, configurations, packages, components
General form of use :
VHDL has several predefined, e.g :
  X’EVENT -- TRUE when there is an event on signal X
  X’LAST_VALUE -- returns the previous value of signal X
  Y’HIGH -- returns the highest value in the range of Y
  X’STABLE(t) -- TRUE when no event has occurred on signal X in the past ‘t’ time
Name’s attribute_identifier -- read as “tick”

## Slide 72: Attributes Register Example
The following example shows hoe attributes can be used to make an 8-bit register
Specifications :
  Triggers on rising clock edge
  Latches only on enable high
  Has a data setup time of x_setup
  Has propagation delay of prop_delay
ENTITY 8_bit_reg IS
GENERIC (x_setup, prop_delay : TIME);
PORT (enable, clk : IN qsim_state;
a : IN qsim_state_vector( 7 DOWNTO 0);
b : OUT qsim_state_vector( 7 DOWNTO 0));
END 8_bit_reg;
qsim_state type is being used-includes logic values 0, 1, X, and Z

## Slide 73: Attributes Register Example (Cont.)
The following architecture is a first attempt at the register
The use of ‘STABLE’ is to used to detect setup violations in the data input
ARCHITECTURE first_attempt OF 8_bit_reg IS
BEGIN
PROCESS (clk)
BEGIN
IF (enable = ‘1’) AND a’STABLE(x_setup) AND (clk = ‘1’) THEN
b <= a AFTER delay;
END IF;
END PROCESS;
END first_attempt;
What happens if a does not satisfy its setup time requirement of x_setup ?

## Slide 74: Attributes Register Example (Cont.)
The following architecture is a second or more robust attempt
The use of ‘LAST_VALUE’ ensures the clcok is rising from a value of ‘0’
ARCHITECTURE behavior OF 8_bit_reg IS
BEGIN
PROCESS (clk)
BEGIN
IF (enable = ‘1’) AND a’STABLE(x_setup) AND (clk = ‘1’) AND
(clk’LAST_VALUE = ‘0’ ) THEN
b <= a AFTER delay;
END IF;
END PROCESS;
END behavior;
A THEN clause could be added to define the behavior when the requirements are not satisfied

## Slide 75: Operators
Operators can be chained to from complex expressions, e.g :
  Can use parentheses for readability and to control the association of operators and operands
Defined precedence levels in decreasing order :
  Miscellaneous operators -- **, abs, not
  Multiplication operators -- *, /, mod, rem
  Sign operator -- +,-
  Addition operators -- sll, srl, sla, sra, rol, ror
  Relational operators -- =, /=, <, <=, >, >=
  Logical operators -- AND, OR, NAND, NOR, XOR, XNOR
res <= a AND NOT(B) OR NOT(a) AND b;

## Slide 76: Operators Examples
The concatenation operator &
VARIABLE shifted, shiftin : BIT_VECTOR( 0 TO 3);
……..
Shifted := shiftin ( 1 TO 3) & ‘0’;
1
0
0
1
0
0
1
0
0 1 2 3
SHIFTEN
SHIFTED
The exponentiation operator **
x := 5 ** 5 -- 5^5
y := 0.5 ** 3
x := 4 ** 0.5 -- illegal
y := 0.5 ** (-2)

## Slide 77: VHDL Examples
Build a library of logic gates
  AND, OR, NAND, NOR, INV, etc
Include sequential elements
  DFF, Register, etc
Include tri-state devices
Use 4-valued logic
  ‘X’, ‘0’, ‘1’, ‘Z’
  Encapsulate global declarations in apackage

## Slide 78: Global Package
PACKAGE resourcees IS
TYPE level IS (‘X’, ‘0’, ‘1’, ‘Z’);
TYPE level_vector IS ARRAY (NATURAL RANGE <> ) OF level;
-- type for vectors (buses)
SUBTYPE delay IS TIME; -- subtype for gate delays
--Functional and procedure declarations go here
END resources;

## Slide 79: Two Input AND Gate Example
USE work.resources.all;
ENTITY and2 IS
GENERIC (trise : delay := 10 ns;
tfall : delay :=8 ns);
PORT( a, b : IN level;
c : OUT level);
END and2;
ARCHITECTURE behav OF and2 IS
BEGIN
one : process (a,b)
BEGIN
IF (a=‘1’ AND b=‘1’) THEN
c <= ‘1’ AFTER trise;
ELSIF (a=‘0’ OR b=‘0’) THEN
c <= ‘0’ AFTER tfall;
ELSE
c <= ‘X’ AFTER (trise + tfall)/2;
END IF;
END process one;

## Slide 80: Tri-State Buffer Example
USE work.resources.all;
ENTITY tri_state IS
GENERIC (trise : delay := 6 ns;
tfall : delay :=5 ns;
this : delay := 8 ns);
PORT( a : IN level;
c : IN level;
b : OUT level);
END tri_state;

## Slide 81: Tri-State Buffer Example (Cont.)
ARCHITECTURE behav OF tri_state IS
BEGIN
one : process (a,c)
BEGIN
IF (c=‘1’ AND a=‘1’) THEN --enable and valid data
b <= ‘1’ AFTER trise;
ELSIF (c=‘1’ AND a=‘0’) THEN
b <= ‘0’ AFTER tfall;
ELSIF (c=‘0’) THEN
b <= ‘Z’ AFTER this;
ELSE -- invalid data or enable
b <= ‘X’ AFTER (trise + tfall)/2;
END IF;
END process one;
END behav;

## Slide 82: D Flip-flop Example
USE work.resources.all;
ENTITY dff IS
GENERIC (tprop : delay := 8 ns;
tsu : delay := 2 ns);
PORT( d : IN level;
clk : IN level;
q : OUT level;
qn : OUT level);
END dff;

## Slide 83
ARCHITECTURE behav OF dff IS
BEGIN
one : process (clk)
BEGIN
IF ( (clk=‘1’ AND clk’LAST_VALUE=‘0’
AND enable = ‘1’ ) THEN --ff enables
IF (d’STABLE (tsu)) THEN -- check valid input data
IF( d=‘0’ ) THEN
q <= ‘0’ AFTER tprop;
qn <= ‘1’ AFTER tprop;
ELSIF (d=‘1’) THEN
q <= ‘1’ AFTER tprop;
qn <= ‘0’ AFTER tprop;
ELSE -- else invalid data
q <= ‘X’;
an <= ‘X’;
END IF;
ELSE -- else violated setup time requirement
q <= ‘X’;
qn <= ‘X’;
END IF;
END IF:
END process one;
END behav;